## Slide 1
SATELLITES, DISTANCE APPROXIMATION, FEASIBILITY TEST, COLLISION DETECTION, SATELLITE HARDWARE, ALGORITHMS IMPLEMENTATION
Capstone Project Phase B
24-2-D-29
Supervisor: Mr. Ilya Zeldner
Shir Cohen 316216340
Yotam Aharon 208608448

## Slide 2
Overview
Introduction 3-4
Background 5-7
Algorithms for Collision Detection 8-10
Goals 11
Solution 12-33
Challenges 34
User Interface 35-38

## Slide 3: Introduction
Satellites
Space debris
Finding possible collisions
Autonomous satellite.
3
2
Background
3
6
7
Verification
plan
4
8
Expected Challenges
Expected results
Solution
Introduction
5
User interface
Algorithms
1
Active\Old Satellites, Space debris 13/03/25
http://astria.tacc.utexas.edu/AstriaGraph/
Active satellite
Inactive satellite
Rocket body
Space debris Uncategorized

## Slide 4: Introduction
Build on prior work titled "Feasibility Analysis and Performance Testing of Collision Detection Algorithms for Satellites”.
Transition from theoretical to practical implementation, focusing on testing algorithms on satellite On-Board Computers (OBC)​.
4
2
Background
3
6
7
Verification
plan
4
8
Expected Challenges
Goals
Solution
Introduction
5
User interface
Algorithms
1

## Slide 5: Background
Finding the future orbit
Propagators
SGP4 Standard General Perturbations Satellite Orbit Model 4
LEMUR2[green] – COSMOS[blue]
5
2
Background
3
6
7
Verification & Testing System
4
8
Challenges
Goals
Solution
Introduction
5
User interface
Algorithms
1

## Slide 6
Graph 1, relative distance and derivative over time
Background
– blue, - red
6
2
Background
3
6
7
Verification
plan
4
8
Challenges
Goals
Solution
Introduction
5
User interface
Algorithms
1

## Slide 7
Processor: ARM Cortex-A76 for real-time collision detection.
Memory: Up to 16GB RAM for high-speed computations.
OS: Linux-based for flexible development and optimization.
Connectivity: Gigabit Ethernet & PCIe for reliable data transfer.
Background – Raspberry Pi 5
7
Raspberry Pi 5 Onboard Computer Front view
Processor: Broadcom BCM2712, Quad-core ARM Cortex-A76, 2.4GHz
RAM: 8GB LPDDR4X-4267
Power: Estimated between 3.5W (idle) and 7.6W (under load)
Cost: $80 USD.
2
Background
3
6
7
Verification
plan
4
8
Challenges
Goals
Solution
Introduction
5
User interface
Algorithms
1

## Slide 8
ANCAS - Alfano Negron Close Approach Software
Cubic polynomial using 4 points
Roots: solving a 3rd degree equation
Algorithms
8
Input:
Output:
for each set of 4 points do:
Map the time points to on the interval
Calculate using the points
Fit cubic polynomial to over
Find the cubic polynomial real roots in the interval
Fit cubic polynomials for in the interval
for each root do:
calculate the distance
if :
end
end
end
2
Background
3
6
7
Verification & Testing System
4
8
Challenges
Goals
Solution
Introduction
5
User interface
Algorithms
1

## Slide 9
Algorithms
9
Input: , ,
Output:
for each set of 4 points do:
Do
Map the time points to on the interval
Calculate using the points
Fit cubic polynomial to over
Find the cubic polynomial real roots in the interval
Fit cubic polynomials for in the interval
for each root do:
calculate the distance at t*
if :
end
end
Sample and at using a propagator
While OR
end
SBO-ANCAS - Alfano Negron Close Approach Software
Cubic polynomial using 4 points
But uses additional points to get better results
Tolerance in time and tolerance in distance
Roots: solving a 3rd degree equation
2
Background
3
6
7
Verification & Testing System
4
8
Challenges
Goals
Solution
Introduction
5
User interface
Algorithms
1

## Slide 10
CATCH - Conjunction Assessment Through Chebyshev Polynomials
Using Chebyshev Proxy Polynomials
N degree polynomial using N+1 points
Roots: finding NxN matrix eigen values
Algorithms
10
2
Background
3
6
7
Verification & Testing System
4
8
Challenges
Goals
Solution
Introduction
5
User interface
Algorithms
1

## Slide 11
Implementing and Deploying the Algorithms
Creating a Testing System
A comprehensive set of experimental results, derived from testing a variety of input types, that will either confirm or refute the feasibility of executing TCA calculations on the satellite's OBC.
Goals
11
11
Introduction
2
Background
3
6
7
Verification & Testing System
4
8
Challenges
Goals
Solution
5
User interface
Algorithms
1

## Slide 12
C++: Chosen for both Tested OBC App and Testing Station App due to efficiency, OOP structure, and compatibility with constrained hardware.
Blazor (C#): Used for GUI development for ease of integration and modern web-based interface.
Development Tools - Programming Languages
12
2
Background
3
6
7
Verification & Testing System
4
8
Challenges
Goals
Solution
Introduction
5
User interface
Algorithms
1

## Slide 13
Eigen: Used for eigenvalue calculations in CATCH’s root-finding algorithm, optimized for low memory usage.
INIH: Lightweight INI file reader for handling configuration files in both applications.
SQLite3: Database solution for local storage, optimized for embedded systems.
SGP4: Satellite orbit propagator used for test data generation and SBO-ANCAS calculations.
Development Tools - External Libraries
13
2
Background
3
6
7
Verification & Testing System
4
8
Challenges
Goals
Solution
Introduction
5
User interface
Algorithms
1

## Slide 14
Implementing and running the algorithms on the satellite On Board Computer.
2 Parts testing system- Tested OBC system and Test Station system.
Comparing algorithms performance
Solution
14
2
Background
3
6
7
Verification & Testing System
4
8
Challenges
Goals
Solution
Introduction
5
User interface
Algorithms
1

## Slide 15: Two Parts Testing System
Test station
Tested on-board computer
User Interface
Test Creation and Management
Results Management
Database
Running tests
Running the algorithms
Testing runtime
15
15
2
Background
3
6
7
Verification & Testing System
4
8
Challenges
Goals
Solution
Introduction
5
User interface
Algorithms
1

## Slide 16: Two Parts Testing System
Test station
Tested on-board computer
16
16
2
Background
3
6
7
Verification & Testing System
4
8
Challenges
Goals
Solution
Introduction
5
User interface
Algorithms
1

## Slide 17: Testing System Communication
17
17
2
Background
3
6
7
Verification & Testing System
4
8
Challenges
Goals
Solution
Introduction
5
User interface
Algorithms
1
Test Request Message Description
Test Results Message Description.
Master-Slave architecture: Testing Station App sends requests, Tested OBC responds.
Defining a communication protocol
Error detection - CRC
Two message types: Test Request Message (from Testing Station to OBC) and Test Results Message (from OBC to Testing Station).

## Slide 18: Communication Methods
18
18
2
Background
3
6
7
Verification & Testing System
4
8
Challenges
Goals
Solution
Introduction
5
User interface
Algorithms
1
Test Request Message Description
Test Results Message Description.
UDP: Fast but unreliable, lacks message order guarantees, requires manual error handling.
Cross Platform TCP: Reliable, ensures correct message order and error-free transmission, used for testing station communication.
Local simulation: Runs independently on a single machine, simulating both the Testing Station and Tested OBC for debugging and testing without actual network communication.

## Slide 19: Testing System Environments
19
19
2
Background
3
6
7
Verification & Testing System
4
8
Challenges
Goals
Solution
Introduction
5
User interface
Algorithms
1
Windows,MacOS, Linux on Raspberry Pi 5
TCP/UDP over localhost, when both systems operate on the same machine.
TCP/UDP over Wi-Fi, when the systems operate on the diffrent machines.
Local Simulation Mode: Simulates communication within the Tested OBC App, enabling test execution without a network connection, supporting asynchronous and self-contained testing.
Feasibility Testing Environments:
Raspberry Pi 5 OBC with Cross Platform TCP over WIFI
CPU Specifications of the Raspberry Pi 5

## Slide 20: Full System Activity Diagram

## Slide 21: Feasibility Testing Data
21
21
2
Background
3
6
7
Verification & Testing System
4
8
Challenges
Goals
Solution
Introduction
5
User interface
Algorithms
1
Catalog of 11,000 active satellites from Celestrak
Catalog test format: One With ALL
Used tests
SBO-ANCAS tolerances: ,
4 variations:
5 days to run the simulation
version | Number of Points Per Segments | Number of segments per minimal revolution
1 | 8 | 8
2 | 8 | 16
3 | 16 | 8
4 | 16 | 16

## Slide 22: Feasibility Testing – Runtime Comparison
22
22
Algorithms Runtime [Sec] per test, only on the first 100 tests for Tmin=8 and 8 points per segment.

## Slide 23: Feasibility Testing – Runtime Comparison
23
23
Algorithms Runtime [Sec] per test, only on the first 100 tests for Tmin=16 and 8 points per segment.

## Slide 24: Feasibility Testing – Runtime Comparison
24
24
Algorithms Runtime [Sec] per test, only on the first 100 tests for Tmin=8 and 16 points per segment.

## Slide 25: Feasibility Testing – Runtime Comparison
25
25
Agorithms Runtime [Sec] per test, only on the first 100 tests for Tmin=16 and 16 points per segment.

## Slide 26: Feasibility Testing – Runtime Comparison
26
26
ANCAS: Linear growth in running times with input size.
SBO‑ANCAS: Consistent increase in run times, dependent on parameters and data characteristics.
CATCH: Steep rise in running times due to high computational costs.

## Slide 27: Feasibility Testing – Error Analysis
27
27
Algorithms distance error [KM] per test in logarithmic scale, only for the tests that passed the defined tolerance 0.00001 for Tmin=8 and 8 points per segment.

## Slide 28: Feasibility Testing – Error Analysis
28
28
Algorithms distance error [KM] per test in logarithmic scale,only for the tests that passed the defined tolerance 0.00001 for Tmin=16 and 8 points per segment.

## Slide 29: Feasibility Testing – Error Analysis
29
29
Algorithms distance error [KM] per test in logarithmic scale, only for the tests that passed the defined tolerance 0.00001 for Tmin=8 and 16 points per segment.

## Slide 30: Feasibility Testing – Error Analysis
30
30
Algorithms distance error [KM] per test in logarithmic scale, only for the tests that passed the defined tolerance 0.00001 for Tmin=16 and 16 points per segment.

## Slide 31: Feasibility Testing – Error Analysis
31
31
ANCAS:
Prioritizes speed but has relatively high error values in distance calculations.
SBO‑ANCAS:
Lowest error values, benefiting from iterative refinement for high accuracy.
Consistently reliable across different test conditions.
CATCH:
Medium-range errors.
Numerical stability issues due to high-degree polynomial calculations, leading to fluctuations in error values.

## Slide 32: Feasibility Testing – Conclusions
32
32
ANCAS: Fastest but least accurate.
SBO-ANCAS: Best balance; consistent high accuracy with moderate runtime.
CATCH: Can reach high accuracy but shows significant runtime cost and sometimes unexpected errors (Further Investigation Needed).
SBO-ANCAS stands out as the most suitable for real-time collision detection due to its balance of speed and precision.

## Slide 33: Overall Conclusions
33
33
Achievements
Implemented and analyzed three algorithms on actual OBC.
Developed a flexible testing system.
Conducted feasibility tests under various input sizes and parameters.
Created a codebase designed for scalability and future expansions.
Unresolved Points & Next Steps
CATCH Behavior: Accuracy vs. runtime conflict remains partially unexplained.
More data and tests required for deeper insight.
Future teams can build on our system to refine and expand the analysis.

## Slide 34: Challenges
Developing Cross Platforms Communication
  Platform-specific implementations.
  “#ifdef” directive with preprocessor defines to compile the required variation each time.
Testing and debugging asynchronous Applications
  Unit tests
  Local Simulations
  Loggers
34
2
Background
3
7
Verification & Testing System
4
8
Challenges
Goals
Solution
Introduction
5
User interface
Algorithms
1
6

## Slide 35: User Interface - Video
35
2
Background
3
7
Verification & Testing System
4
8
Challenges
Goals
Solution
Introduction
5
User interface
Algorithms
1
6

## Slide 36: User Interface- Home Page

## Slide 37: User Interface- Create Test

## Slide 38: User Interface- Test Results

## Slide 39: Bibliography
[1] Alfano, S. (1994). Determining Satellite Close Approaches-Part II. ADVANCES IN THE ASTRONAUTICAL SCIENCES, 87, 233 -233. ANCAS
[2] Denenberg, E. (2020). Satellite closest approach calculation through chebyshev proxy polynomials. Acta Astronautica, 170, 55-65. SBO-ANCAS
[3] Denenberg, E., & Gurfil, P. (2016). Improvements to time of closest approach calculation. Journal of Guidance, Control, and Dynamics, 39(9), 1967-1979. CATCH
[4] AstariaGraph satellites and space debris visual map : http://astria.tacc.utexas.edu/AstriaGraph/
[5] CelesTrak: https://celestrak.org/
[6] CelesTrak Current Data: https://celestrak.org/NORAD/elements/index.php?FORMAT=tle
[7] The gem5 simulator: https://www.gem5.org/
[8] ISISPACE OBC: https://www.isispace.nl/product/on-board-computer/
[9] NASA on orbital debris: NASA
[10] Our GitHub repository: https://github.com/cohensh96/Satellite-s-project
2
Background
3
6
7
Verification & Testing System
4
8
Challenges
Expected results
Solution
Introduction
5
User interface
Algorithms
1

## Slide 40: Thank You!
Do you have any questions?