## Slide 1
SATELLITES, DISTANCE APPROXIMATION, FEASIBILITY TEST, COLLISION DETECTION, SATELLITE HARDWARE, ALGORITHMS IMPLEMENTATION
Capstone Project Phase A
24-2-D-29
Supervisor: Mr. Ilya Zeldner
Shir Cohen 316216340
Yotam Aharon 208608448

## Slide 2
Overview
Introduction 3-4
Background 5-6
Algorithms for Collision Detection 7-10
Expected Results 11
Solution 12-20
Expected Challenges 21
Verification and Validation 22
User Interface 23-24

## Slide 3: Introduction
Satellites
Space debris
Finding possible collisions
Autonomous satellite.
3
2
Background
3
6
7
Verification
plan
4
8
Expected Challenges
Expected results
Solution
Introduction
5
User interface
Algorithms
1
Active\Old Satellites, Space debris 19/09/24
http://astria.tacc.utexas.edu/AstriaGraph/
Active satellite
Inactive satellite
Rocket body
Space debris Uncategorized

## Slide 4: Introduction
Build on prior work titled "Feasibility Analysis and Performance Testing of Collision Detection Algorithms for Satellites”.
Transition from theoretical to practical implementation, focusing on testing algorithms on satellite On-Board Computers (OBC)​.
4
2
Background
3
6
7
Verification
plan
4
8
Expected Challenges
Expected results
Solution
Introduction
5
User interface
Algorithms
1

## Slide 5: Background
Finding the future orbit
Propagators
SGP4 Standard General Perturbations Satellite Orbit Model 4
LEMUR2[green] – COSMOS[blue]
5
2
Background
3
6
7
Verification
plan
4
8
Expected Challenges
Expected results
Solution
Introduction
5
User interface
Algorithms
1

## Slide 6
Graph 1, relative distance and derivative over time
Background
– blue, - red
6
2
Background
3
6
7
Verification
plan
4
8
Expected Challenges
Expected results
Solution
Introduction
5
User interface
Algorithms
1

## Slide 7
ANCAS - Alfano Negron Close Approach Software
Cubic polynomial using 4 points
Roots: solving a 3rd degree equation
Algorithms
7
Input:
Output:
for each set of 4 points do:
Map the time points to on the interval
Calculate using the points
Fit cubic polynomial to over
Find the cubic polynomial real roots in the interval
Fit cubic polynomials for in the interval
for each root do:
calculate the distance
if :
end
end
end
2
Background
3
6
7
Verification
plan
4
8
Expected Challenges
Expected results
Solution
Introduction
5
User interface
Algorithms
1

## Slide 8
Algorithms
8
Input: , ,
Output:
for each set of 4 points do:
Do
Map the time points to on the interval
Calculate using the points
Fit cubic polynomial to over
Find the cubic polynomial real roots in the interval
Fit cubic polynomials for in the interval
for each root do:
calculate the distance at t*
if :
end
end
Sample and at using a propagator
While OR
end
SBO-ANCAS - Alfano Negron Close Approach Software
Cubic polynomial using 4 points
But uses additional points to get better results
Tolerance in time and tolerance in distance
Roots: solving a 3rd degree equation
2
Background
3
6
7
Verification
plan
4
8
Expected Challenges
Expected results
Solution
Introduction
5
User interface
Algorithms
1

## Slide 9
CATCH - Conjunction Assessment Through Chebyshev Polynomials
Using Chebyshev Proxy Polynomials
N degree polynomial using N+1 points
Roots: finding NxN matrix eigen values
Algorithms
9
2
Background
3
6
7
Verification
plan
4
8
Expected Challenges
Expected results
Solution
Introduction
5
User interface
Algorithms
1

## Slide 10
A comprehensive set of experimental results, derived from testing a variety of input types, that will either confirm or refute the feasibility of executing TCA calculations on the satellite's OBC.
Optimized and reliable implementations of the CATCH algorithm, ready for integration into the satellite system when necessary.
Expected result
10
10
Introduction
2
Background
3
6
7
Verification
plan
4
8
Expected Challenges
Expected results
Solution
5
User interface
Algorithms
1
Notes: In this project we expect to finish with concrete and comprehensive proof of feasibility or infeasibility of the task of running the TCA calculations on the satellite OBC.
Feasibility test of : Implementing the algorithms
Running on the Tested OBC
Analyzing the result

## Slide 11
2 Parts testing system- Tested OBC system and Test Station system.
Comparative Analysis of Satellite Boards for Algorithm Testing.
Optimization of Eigenvalue Calculation in the CATCH Algorithm.
Implementing and running the algorithms on the satellite On Board Computer.
Solution
11
2
Background
3
6
7
Verification
plan
4
8
Expected Challenges
Expected results
Solution
Introduction
5
User interface
Algorithms
1

## Slide 12
12
Optimization of Eigenvalue Calculation
The Companion Matrix [[2],Eq.20]
Sparse Matrix
Near Tridiagonal
Fixed Number of Values in finite range [-1,1]
The memory on the satellite board is limited, so we don't want to use libraries for calculations.
We prefer to implement this ourselves based on our limitations.
Aim to decrease the number of operations and reducing runtime.
2
Background
3
6
7
Verification
plan
4
8
Expected Challenges
Expected results
Solution
Introduction
5
User interface
Algorithms
1
Notes: Companion Matrix A:
Sparse Structure: Primarily zeros, reducing storage and computational demands.
Tridiagonal Form: Non-zero elements located on the first sub diagonal and super diagonal.
Fixed Number of Values: The matrix composition is defined by a set number of specific values in range [-1,1] , facilitating predictable computational behavior.
Computational Considerations:
Reducing Operations: Aim to decrease the number of operations, enhancing faster convergence and reducing runtime, particularly for onboard systems
Ongoing Investigation:
Experimental Approaches: Testing various methods to reduce operation count while preserving accuracy.
Potential Impact: Enhancements could significantly improve real-time assessments in satellite operations.

## Slide 13
Our goal was to identify an alternative board that closely matched the specifications of the ISIS OBC.
By choosing a weaker satellite on-board computer we can achieve the following goals:
Reduce Costs: select less powerful computers, avoiding excess capabilities.
Test Performance: Ensure algorithms function well even in resource-limited settings.
Prove Feasibility: If it works with less, it will work with more.
Comparative Analysis of Satellite Boards
13
2
Background
3
6
7
Verification
plan
4
8
Expected Challenges
Expected results
Solution
Introduction
5
User interface
Algorithms
1
Notes: Reduce Costs: select less powerful computers, avoiding excess capabilities.
Test Performance: Ensure algorithms function well even in resource-limited settings.
Prove Feasibility: If it works with less, it will work with more.

## Slide 14
The TS-7553 OBC identified as the closest match to the ISIS OBC (processor architecture, memory, and storage).
Offers slightly lower performance, which aligns with our goal of testing in a constrained environment.
Ensures that any optimizations we make will be applicable to the more advanced ISIS OBC, providing relevant and transferable results.
The Selected TS-7553 OBC
14
TS-7553 Onboard Computer Front view
Processor: 250MHz ARM9
RAM: 64MB DDR2
Power: 3.2W
Cost: $180 USD.
Modifications: Requires additional MicroSD and FRAM
2
Background
3
6
7
Verification
plan
4
8
Expected Challenges
Expected results
Solution
Introduction
5
User interface
Algorithms
1

## Slide 15: Two Parts Testing System
Test station
Tested on-board computer
User Interface
Test Creation and Management
Results Management
Database
Running tests
Running the algorithms
Testing runtime
15
15
2
Background
3
6
7
Verification
plan
4
8
Expected Challenges
Expected results
Solution
Introduction
5
User interface
Algorithms
1

## Slide 16: Wired Communication Strategy for Testing TS-7553 OBC
16
16
We will use Ethernet for our system to ensure stable and efficient wired communication between the TS-7553 OBC and the Test Station.
High Data Transfer Rates: Supports up to 1 Gbps for efficient, large data transfers.
Low Latency: Essential for real-time performance testing and prompt algorithm evaluation.
Reliability: Offers stability for continuous, high-volume data exchanges.
The TS-7553 OBC is equipped with an Ethernet port, which allows us to utilize this method without needing additional adapters
2
Background
3
6
7
Verification
plan
4
8
Expected Challenges
Expected results
Solution
Introduction
5
User interface
Algorithms
1

## Slide 17: Full System Use Case
17
2
Background
3
6
7
Verification
plan
4
8
Expected Challenges
Expected results
Solution
Introduction
5
User interface
Algorithms
1

## Slide 19: Expected Challenges
Limited Processing Power and Memory Constraints.
Real-Time Performance and Latency.
Data Loss and Transmission Errors.
19
2
Background
3
7
Verification
plan
4
8
Expected Challenges
Expected results
Solution
Introduction
5
User interface
Algorithms
1
6

## Slide 20: User Interface
Home Page
Create test window

## Slide 21: User Interface
Test result window
Active Test view

## Slide 22: Verification plan
Test Station
Tested OBC
# | Test description | Expected result
1 | Error in the input data: wrong input data (TLE, either one of the 2 required TLE or both) | No experiment is initiated, error message to the user.
2 | Error in the input data: Missing test variable (Number of iterations, CATCH polynomial degree) | No experiment is initiated, error message to the user.
3 | MSS (main success scenario), correct input values (TLE, variables). | Send correct message and data, save the correct result received from the simulation.
4 | Communication error: receive error message from the Tested OBC (simulated). | Try to send the data again, display error message to the user on repetitive errors.
5 | Communication error: no communication with the Tested OBC. | Display error message to the user.
# | Test description | Expected result
1 | Error in the input data: missing\out of bound test variables. | Send back error message.
2 | Error in the input data: missing data points (missing some of the values for a points in time data composed from r1,v1,r2,v2,t) | Send back error message.
3 | MSS (main success scenario) variations (run ANCAS/CATCH), correct input values (test variables, test data set). | Send back correct result.
4 | Communication error: receive error message from the Testing station. | Try to send the result message again, give up after repetitive errors.
5 | Communication error: no communication from the Testing station | Wait for the station response.
22
Testing using Bottom-Up methodology
2
Background
3
6
7
Verification
plan
4
8
Expected Challenges
Expected results
Solution
Introduction
5
User interface
Algorithms
1

## Slide 23: Bibliography
[1] Alfano, S. (1994). Determining Satellite Close Approaches-Part II. ADVANCES IN THE ASTRONAUTICAL SCIENCES, 87, 233 -233. ANCAS
[2] Denenberg, E. (2020). Satellite closest approach calculation through chebyshev proxy polynomials. Acta Astronautica, 170, 55-65. SBO-ANCAS
[3] Denenberg, E., & Gurfil, P. (2016). Improvements to time of closest approach calculation. Journal of Guidance, Control, and Dynamics, 39(9), 1967-1979. CATCH
[4] AstariaGraph satellites and space debris visual map : http://astria.tacc.utexas.edu/AstriaGraph/
[5] CelesTrak: https://celestrak.org/
[6] CelesTrak Current Data: https://celestrak.org/NORAD/elements/index.php?FORMAT=tle
[7] The gem5 simulator: https://www.gem5.org/
[8] ISISPACE OBC: https://www.isispace.nl/product/on-board-computer/
[9] NASA on orbital debris: NASA
[10] Our GitHub repository: https://github.com/cohensh96/Satellite-s-project
2
Background
3
6
7
Verification
plan
4
8
Expected Challenges
Expected results
Solution
Introduction
5
User interface
Algorithms
1

## Slide 24: Thank You!
Do you have any questions?